## Slide 1: Pipeline: Introduction
Theseslides arederivedfrom: CSCE430/830Computer
ArchitecturecoursebyProf. Hong Jiang andDavePaterson©UCB
Somefiguresandtables have be nderivedfrom : ComputerSystem Architectureby M.MorrisMano

## Slide 2: Pipelining Outline
Introduction Defining Pipelining Pipelining Instructions
Hazards
Structural hazards Data Hazards Control Hazards

## Slide 3: What is Pipelining?
A way of speeding up execution of instructions
Key idea:
overlap execution of multiple instructions

## Slide 4: The Laundry Analogy
●
Ann, Brian, Cathy, Dave
each have one load of clothes to wash, dry, and fold
●
Washer takes 30 minutes
●
Dryer takes 30 minutes
●
“Folder” takes 30 minutes
●
“Stasher” takes 30 minutes to put clothes into drawers
A B C D

## Slide 5: If we do laundry sequentially...
●
●
30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
9
6 PM 12
7 8 10 11 1
Time
A
B
T
a s k
O
r C
d e r
D
2 AM

## Slide 6: To Pipeline, We Overlap Tasks
12
6 PM 12 2 AM
9
7 8 10 11 1
Time
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest
pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
30
30 30 30 30 30 30
A
C
T
a s k
O
r d
e D
r
B
•
•
•
•
•
•

## Slide 7: Pipelining a Digital System
●
●
●
Key idea: break big computation up into pieces
1ns
Separate each piece with a pipeline register
200ps
200ps
200ps
200ps
200ps
Pipeline Register

## Slide 8: Pipelining a Digital System
Why do this? Because it's faster for repeated computations
1ns
Non-pipelined: 1operationfinishes every1ns
200ps
200ps
200ps
200ps
200ps
Pipelined: 1operationfinishes every200ps

## Slide 9: Comments about pipelining
Pipelining increases throughput, but not latency Answer available every 200ps, BUT
-A single computation still takes 1ns Limitations:
-Computations must be divisible into stage size
-Pipeline registers add overhead

## Slide 10: Suppose we need to perform multiply and add operation with a stream of numbers
●
●
●
Each subinstruction is implemented in a segment within the pipeline. Each segment has one or two regsiters and a combinational circuit
The sub operations performed in each segement are as follows
●
●
●

## Slide 11: Example of Pipeline Processing

## Slide 12: Content of Registers in Pipeline

## Slide 13: Space Time Diagram of Pipeline

## Slide 14: Speedup
Speedup from pipeline
= Average instruction time unpiplined/Average instruction time pipelined
Consider a case for k-segment pipeline with a clock cycle time tp to execute n tasks. The first task T1 requires a time equal to k*tp to complete its operation since there are k segments in pipeline. The remaining n-1 tasks emerge from the pipe at a rate of one task per clock cycle and they will be completed in k+n-1 clock cycles.
Next, to concsider an unpipeline unit that performs the same operation and takes a time equal to tn to complete the task. The total time required fro n tasks is n*tn. The speed up of a pipeline processing over an equivalent non-pipeline processing is defined by the ratio

## Slide 15: Speedup
●
As the number of tasks increase n becomes much larger than k-1, and k+n-1 approaches
the value of n. Under this condition, the speed up becomes
●
If we assume the the time taken to process the task is the same as in the pipeline and nonpipeline circuits, we will have
The speedup then reduces to numer of stages of pipeline
●

## Slide 16: Pipelining a Processor
Recall the 5 steps in instruction execution:
  Instruction Fetch (IF)
  Instruction Decode and Register Read (ID)
  Execution operation or calculate address (EX)
  Memory access (MEM)
  Write result into register (WB)
Review: Single-Cycle Processor
All 5 steps done in a single clock cycle
Dedicated hardware required for each step

## Slide 17: Review - Single-Cycle Processor

## Slide 18: The Basic Pipeline For MIPS
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1Cycle 2 Cycle 3 Cycle 4Cycle 5 Cycle 6Cycle 7
I
n s t r.
O
r d e r

## Slide 19: Basic Pipelined Processor

## Slide 20: Single-Cycle vs. Pipelined Execution
Non-Pipelined
20
40
60
80 10 0 120 140 160 180
lw | $1, | 100($0)
lw | $2, | 200($0)
lw | $3, | 300($0)
Instruction Fetch
REG RD
ALU
REG WR
MEM
Instruction Fetch
REG RD
REG WR
ALU MEM
Instruction
Fetch
Time
Instruction 0
Order
80 ps
80 ps
80 ps
Pipelined
0 20
40
60
80 10 0 120 140 160
lw | $1, | 100($0)
lw | $2, | 200($0)
lw | $3, | 300($0)
Instruction Fetch
REG RD
ALU
REG WR
MEM
Time
Instruction
Order
20 ps
Instruction Fetch
REG RD
ALU
REG WR
MEM
Instruction Fetch
REG RD
ALU
REG WR
MEM
20 ps
20 ps 20 ps 20 ps 20 ps 20 ps

## Slide 21: Comments about Pipelining
The good news
Multiple instructions are being processed at same time
This works because stages are isolated by registers
Best case speedup of N
The bad news
- Instructions interfere with each other - hazards
Example: different instructions may need the same piece of hardware (e.g., memory) in same clock cycle
Example: instruction may require a result produced by an earlier instruction that is not yet complete

## Slide 22: Pipeline Hazards
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
Structural hazards: two different instructions use same h/w in same cycle
Data hazards: Instruction depends on result of prior instruction still in the pipeline
Control hazards: Pipelining of branches & other instructions that change the PC

## Slide 23: Why it’s important…
If you're a hardware designer OR a complier writer, you need to be aware of how HLL is mapped to assembly instructions AND what HW is used to execute a sequence of assembly instructions
Otherwise, it is quite possible to always have built in inefficiencies

## Slide 24: Pipelining hazards
Pipeline hazards prevent next instruction from executing during designated clock cycle
There are 3 classes of hazards:
  Structural Hazards:
    Arise from resource conflicts
    HW cannot support all possible combinations of instructions
  Data Hazards:
    Occur when given instruction depends on data from an instruction ahead of it in pipeline
  Control Hazards:
    Result from branch, other instructions that change flow of program (i.e. change PC)

## Slide 25: How do we deal with hazards?
Often, pipeline must be stalled
Stalling pipeline usually lets some instruction(s) in pipeline proceed, another/others wait for data, resource, etc.
A note on terminology:
  If we say an instruction was “issued later than instruction x”, we mean that it was issued after instruction x and is not as far along in the pipeline
  If we say an instruction was “issued earlier than instruction x”, we mean that it was issued before instruction x and is further along in the pipeline

## Slide 26: Stalls and performance
Stalls impede progress of a pipeline and result in deviation from 1 instruction executing/clock cycle
Pipelining can be viewed to:
  Decrease CPI or clock cycle time for instruction
  Let’s see what affect stalls have on CPI…
CPI pipelined =
  Ideal CPI + Pipeline stall cycles per instruction
  1 + Pipeline stall cycles per instruction

## Slide 27: Stalls and performance
Ignoring overhead and assuming stages are balanced:
If no stalls, speedup equal to # of pipeline stages in ideal case

## Slide 28: STRUCTURAL HAZARDS

## Slide 29: Structural hazards
Avoid structural hazards by duplicating resources
– e.g. an ALU to perform an arithmetic operation and an adder to increment PC
If not all possible combinations of instructions can be executed, structural hazards occur
Pipelines stall result of hazards, CPI increased from the usual “1”

## Slide 30: An example of a structural hazard
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
Time
ALU
Reg
Mem
DM
Reg
Load
Instruction 1
Instruction 2
Instruction 3
Instruction 4
What’s the problem here?

## Slide 31: How is it resolved?
Time
ALU
Reg
Mem
DM
Reg
Load
Instruction 1
Instruction 2
Stall
Instruction 3
Bubble
Bubble
Bubble
Bubble
Bubble
Pipeline generally stalled by
inserting a “bubble” or NOP
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg

## Slide 32: Or alternatively…
Inst. # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LOAD | IF | ID | EX | MEM | WB |  |  |  |  | 
Inst. i+1 |  | IF | ID | EX | MEM | WB |  |  |  | 
Inst. i+2 |  |  | IF | ID | EX | MEM | WB |  |  | 
Inst. i+3 |  |  |  | stall | IF | ID | EX | MEM | WB | 
Inst. i+4 |  |  |  |  |  | IF | ID | EX | MEM | WB
Inst. i+5 |  |  |  |  |  |  | IF | ID | EX | MEM
Inst. i+6 |  |  |  |  |  |  |  | IF | ID | EX
Clock Number
LOAD instruction “steals” an instruction fetch cycle which will cause the pipeline to stall.
Thus, no instruction completes on clock cycle 8

## Slide 33: What’s the realistic solution?
Answer: Add more hardware.
  (especially for the memory access example – i.e. the common case)
    CPI degrades quickly from our ideal ‘1’ for even the simplest of cases…

## Slide 34: DATA HAZARDS

## Slide 35: Data hazards
These exist because of pipelining
Why do they exist???
  Pipelining changes when data operands are read, written
  Order differs from order seen by sequentially executing instructions on un-pipelined machine
Consider this example:
  ADD R1, R2, R3
  SUB R4, R1, R5
  AND R6, R1, R7
  OR R8, R1, R9
– XOR R10, R1, R11
All instructions after ADD use result of ADD
ADD writes the register in WB but SUB needs it in ID.
This is a data hazard

## Slide 36: Illustrating a data hazard
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
Mem
ADD R1, R2, R3
SUB R4, R1, R5
AND R6, R1, R7
OR R8, R1, R9
XOR R10, R1, R11
ALU
Reg
Mem
Time
ADD instruction causes a hazard in next 3 instructions b/c register not written until after those 3 read it.
CC 1 CC 2 CC 3 CC 4
CC 5 CC 6

## Slide 37: Forwarding
Problem illustrated on previous slide can actually be solved relatively easily – with forwarding
Can we move the result from EX/MEM register to the beginning of ALU (where SUB needs it)?
  Yes!
Generally speaking:
  Forwarding occurs when a result is passed directly to functional unit that requires it.
  Result goes from output of one unit to input of another

## Slide 38: When can we forward?
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
Mem
Time
ADD R1, R2, R3
SUB R4, R1, R5
AND R6, R1, R7
OR R8, R1, R9
XOR R10, R1, R11
ALU
Reg
Mem
SUB gets info. from EX/MEM pipe register
AND gets info. from MEM/WB pipe register
OR gets info. by forwarding from register file
Rule of thumb:
If line goes “forward” you can do forwarding.
If its drawn backward, it’s physically impossible.

## Slide 39: Forwarding doesn’t always work
ALU
Reg
IM
DM
Reg
ALU
Reg
IM
DM
ALU
Reg
IM
Time
LW R1, 0(R2)
SUB R4, R1, R5
AND R6, R1, R7
OR R8, R1, R9
Reg
IM
Can’t get data to subtract b/c result needed at beginning of CC #4, but not produced until end of CC #4.
Load has a latency that forwarding can’t solve.
Pipeline must stall until hazard cleared (starting with instruction that wants to use data until source produces it).

## Slide 40: The solution pictorially
ALU
Reg
IM
DM
Reg
Reg
IM
IM
Time
LW R1, 0(R2)
SUB R4, R1, R5
AND R6, R1, R7
OR R8, R1, R9
Bubble
Bubble
Bubble
ALU
Reg
Reg
IM
ALU
DM
Insertion of bubble causes # of cycles to complete this sequence to grow by 1

## Slide 41: HW Change for Forwarding
Idea: send result just calculated back around to ALU inputs
Send output of memory back to ALU too…

## Slide 42: Data hazard specifics
There are actually 3 different kinds of data hazards:
  Read After Write (RAW)
  Write After Write (WAW)
  Write After Read (WAR)
With an in-order issue/in-order completion machine, we’re not as concerned with WAW, WAR

## Slide 43: Read after write (RAW) hazards
With RAW hazard, instruction j tries to read a source operand before instruction i writes it.
Thus, j would incorrectly receive old or incorrect value
Graphically/Example:
Can use stalling or forwarding to resolve this hazard
…
j
i
…
Instruction j is a read instruction issued after i
Instruction i is a write instruction issued before j
i: ADD R1, R2, R3
j: SUB R4, R1, R6

## Slide 44: Memory Data Hazards
Seen register hazards, can also have memory hazards
  RAW:
    store R1, 0(SP)
    load R4, 0(SP)
In simple pipeline, memory hazards are easy
  In order, one at a time, read & write in same stage
In general though, more difficult than register hazards
 | 1 | 2 | 3 | 4 | 5 | 6
Store R1, 0(SP) | F | D | EX | M | WB | 
Load R1, 0(SP) |  | F | D | EX | M | WB

## Slide 45: Data hazards and the compiler
Compiler should be able to help eliminate some stalls caused by data hazards
i.e. compiler could not generate a LOAD instruction that is immediately followed by instruction that uses result of LOAD’s destination register.

## Slide 46: What about control logic?
For MIPS integer pipeline, all data hazards can be checked during ID phase of pipeline
If data hazard, instruction stalled before its issued
Whether forwarding is needed can also be determined at this stage, controls signals set
If hazard detected, control unit of pipeline must stall pipeline and prevent instructions in IF, ID from advancing

## Slide 47: Some example situations
Situation | Example | Action
No Dependence | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R6, R7 OR R9, R6, R7 | No hazard possible because no dependence exists on R1 in the immediately following three instructions.
Dependence requiring stall | LW R1, 45(R2) ADD R5, R1, R7 SUB R8, R6, R7 OR R9, R6, R7 | Comparators detect the use of R1 in the ADD and stall the ADD (and SUB and OR) before the ADD begins EX
Dependence overcome by forwarding | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R1, R7 OR R9, R6, R7 | Comparators detect the use of R1 in SUB and forward the result of LOAD to the ALU in time for SUB to begin with EX
Dependence with accesses in order | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R6, R7 OR R9, R1, R7 | No action is required because the read of R1 by OR occurs in the second half of the ID phase, while the write of the loaded data occurred in the first half.

## Slide 48: Detecting Data Hazards

## Slide 49: Hazards vs. Dependencies
dependence: fixed property of instruction stream
  (i.e., program)
hazard: property of program and processor organization
  implies potential for executing things in wrong order
    potential only exists if instructions can be simultaneously “in-flight”
    property of dynamic distance between instructions vs. pipeline depth
For example, can have RAW dependence with or without hazard
  depends on pipeline

## Slide 50: CONTROL HAZARDS

## Slide 51: Branch / Control Hazards
So far, we’ve limited discussion of hazards to:
  Arithmetic/logic operations
  Data transfers
Also need to consider hazards involving branches:
– Example: |  | 
40: beq | $1, $3, 28 | # (28 leads to address 72)
44: and | $12, $2, $5 | 
48: or | $13, $6, $2 | 
52: add | $14, $2, $2 | 
72: lw | $4, 50($7) | 
How long will it take before the branch decision takes effect?
– What happens in the meantime?

## Slide 52: How branches impact pipelined instructions
If branch condition true, must skip 44, 48, 52
  But, these have already started down the pipeline
  They will complete unless we do something about it
How do we deal with this?
  We’ll consider 2 possibilities

## Slide 53: Dealing w/branch hazards: always stall
Branch taken
  Wait 3 cycles
  No proper instructions in the pipeline
  Same delay as without stalls (no time lost)

## Slide 54: Dealing w/branch hazards: always stall
Branch not taken
  Still must wait 3 cycles
  Time lost
  Could have spent CCs fetching, decoding next instructions

## Slide 55: Dealing w/branch hazards
On average, branches are taken ½ the time
  If branch not taken…
    Continue normal processing
  Else, if branch is taken…
    Need to flush improper instruction from pipeline
One approach:
  Always assume branch will NOT be taken
    Cuts overall time for branch processing in ½
  If prediction is incorrect, just flush the pipeline

## Slide 56: Impact of “predict not taken”
Execution proceeds normally – no penalty

## Slide 57: Impact of “predict not taken”
Bubbles injected into 3 stages during cycle 5

## Slide 58: Branch Prediction
Prior solutions are “ugly”
Better (& more common): guess possible outcome
  Technique is called “branch predicting”; needs 2 parts:
    “Predictor” to guess where / if instruction will branch
      (and to where)
    “Recovery Mechanism”:
      i.e. a way to fix your mistake
  Prior strategy:
    Predictor: always guess branch never taken
    Recovery: flush instructions if branch taken
  Alternative: accumulate info. in IF stage as to…
    Whether or not for any particular PC value a branch was taken next
    To where it is taken
    How to update with information from later stages

## Slide 59: A Branch Predictor

## Slide 60: Predictor for a Single Branch
state
2. Predict Output T/NT
1. Access
3. Feedback T/NT
T
Predict Taken
Predict Taken
1
0
T
NT
General Form
1-bit prediction
NT
PC
Feedback

## Slide 61: Branch History Table of 1-bit Predictor
BHT also called branch prediction buffer
Can use only one 1-bit predictor, but accuracy is low
BHT: use a table of simple predictors, indexed by bits from PC
More entries, more cost, but less conflicts, higher accuracy
BHT can contain complex predictors
Prediction
K-bit
Branch
address
2k

## Slide 62: 1 bit weakness
Example:
– in a loop, 1-bit BHT will cause 2 mispredictions
Consider a loop of 9 iterations before exit:
for (…){
for (i=0; i<9; i++) a[i] = a[i] * 2.0;
}
  End of loop case, when it exits instead of looping as before
  First time through loop on next time through code, when it predicts exit instead of looping
  Only 80% accuracy even if loop 90% of the time

## Slide 63: 2-bit saturating counter
NT
Predict Taken
Predict Not Taken
Predict Taken
Predict Not Taken
11
10
01
00
NT
T
NT
T
T NT
Solution: 2-bit scheme where change prediction only if get misprediction twice:
T
Blue: stop, not taken
Gray: go, taken
Adds hysteresis to decision making process

## Slide 64: Branch target buffer
48
Branch Target Buffer (BTB): Address of branch index to get prediction AND branch address (if taken)
– Note: must check for branch match now, since can’t use wrong branch address
Example: BTB combined with BHT
Branch PC Predicted PC
=?
PC of instruction FETCH
Extra prediction state bits
Yes: instruction is branch and use predicted PC as next PC
No: branch not
predicted, proceed normally
(Next PC = PC+4)

## Slide 65: Discussion
65
How does instruction set design impact pipelining?
Does increasing the depth of pipelining always increase performance?

## Slide 66: Comparative performance
51
Throughput: instructions per clock cycle = 1/cpi
  Pipeline has fast throughput and fast clock rate
Latency: inherent execution time, in cycles
  High latency for pipelining causes problems
    Increased time to resolve hazards
Board

## Slide 67: Technique to reduce branch penalties
Branch delay slot: Location following branch instruction
If execution of branch instruction takes more than one step in pipeline, branch penalty can be reduced by executing instruction in delay slot before branch decision is made.
This concept is called delayed branch, as if the branch execution is delayed by one cycle.

## Slide 68: Reducing branch penalties (cont.)
Useful instructions kept in delay slots which are fully executed whether or not branch is taken.
Program executes as if branch instruction was placed after instructions in delay slot.
If no suitable instructions can be put in delay slots, it is filled with instructions which do no-operations. For example, Add R1,0,R1, which does not effect any register or flag.

## Slide 69: Control Hazards
• Branches require stalls as they are not resolved till the execution
• Conditional branches are even more difficult
• Every fifth instruction executed is typically a branch in compiled programs
ADD R1,R2,R3
BEQZ R2,X
Delay Slot
..
X:
------
BEQZ R2,X
ADD R1,R2,R3
Delay Slot
…
X

## Slide 70: Delayed branch
X: SUB R4,R5,R6 X: ADD R1,R2,R3
ADD R1,R2,R3 BEQZ R1,X
BEQZ R1,X SUB R4,R5,R6
Is this correct?

## Slide 71: Instruction Level Parallelism
Constraints
Typically every 6th instruction is a branch
Exploitation of ILP cannot be based on these six instructions alone

## Slide 72: Advanced Techniques
Loop unrolling
Basic pipeline scheduling
Dynamic scheduling
Register renaming
Branch prediction
Multiple issue of instructions
Dependence analysis at compilation
Software pipeline
Memory pipeline

## Slide 73: Instruction Queue
Fetch Unit: to supply the execution unit with steady stream of instructions.
Stream may be interrupted due to cache miss, data dependency or branch instruction.
Instruction following unconditional branch can not be fetched until decoding of branch instruction and computation of target address.
In conditional branch, the conditional has to be evaluated before fetching next instruction.
Sophisticated fetch units used to fetch several instructions before they are needed and maintain instruction queue.
A dispatch unit takes instructions from the front of the queue and sends them to free execution units.

## Slide 74: Instruction Queue

## Slide 75: Multiple execution units
Several parallel units for a stage of pipeline