## Slide 1
Introduction to Computer Organization
Welcome
Instructors:
Ajai Jain
Pranab Roy

## Slide 2: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc. Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in Bluespec Verilog (BSV) Computer Organization
2/16

## Slide 3: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc.
Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in Bluespec Verilog (BSV) Computer Organization
2/16

## Slide 4: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc. Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in Bluespec Verilog (BSV) Computer Organization
2/16

## Slide 5: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc. Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in Bluespec Verilog (BSV) Computer Organization
2/16

## Slide 6: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc. Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in Bluespec Verilog (BSV) Computer Organization
2/16

## Slide 7: Basics
Required Background
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc. Binary number system and operations
What will be covered?
Programming using Assembly Language Circuit descriptions in VHDL
2/16

## Slide 8
Lectures:
Wednesday, Thursday, Friday; 10:00 AM - 10:50 AM, EB-102
Labs:
Groups of 2-3 students
New language for design descriptions: VHDLAssembly language programming

## Slide 9
Required Background (Let me know if you don’t have it)
Programming (Native Compilation techniques)
Pick up C/C++ if not known already.
Knowledge of digital gates, flip-flops, latches, counters etc ?
Binary number system and operations

## Slide 10: Grading Policy Attendance: 5 Quizzes (announced or unannounced) : 10 Assignment : 10 Mid Semester Exam : 20 End Semester Exam : 30 Lab (Continuous Evaluation): 10 Lab (End Sem) : 15

## Slide 11
Course Material:
No text books
Follow the lecture notes very closely
Reference Books
Assembly Language: Online notes http://asm.sourceforge.net/ http://chortle.ccsu.edu/AssemblyTutorial/index.html
Computer Organization:
Patterson, Hannessy: Computer Organization and Design Hamacher et.al.: Computer Organization
Tanenbaum: Structured Computer Organization Parhami: Computer Architecture
Stallings: Computer Organization and Architecture

## Slide 12: Give feed back through out the semester Feel free to discuss anything with the instructor including criticism of instructor, TAs Participate in the discussion : No question is silly enough

## Slide 13: Logistics
Keep checking the course web page for announcements. Do not be late for the class
Keep your cell phones switched off
7/16

## Slide 14: DO NOT CHEAT
I follow zero tolerance policy.
Straight F for copying in assignment
I do not distinguish between the source and the destination nodes of the copy edge.
Names are also reported to authorities to be put in personal files.

## Slide 15
Any Questions/Comments/Suggestions?

## Slide 16: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Basic Circuits
10/16

## Slide 17: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Basic Circuits
10/16

## Slide 18: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 19: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 20: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 21: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 22: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 23: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 24: Review of Digital Circuits
Basic Gates
AND, OR, NAND, NOR, XOR, XNOR, NOT, BUF
Memory Elements Latch, Flip Flops Registers
Level Sensitive, Edge Triggered
Input output behaviour (Parallel or Serial): SISO (Delay Line), SIPO, PISO, PIPO
Basic Circuits
Multiplexers, Counters, ALU, Adders, Multipliers
10/16

## Slide 25: Transistor: Building Block of Computers
Microprocessors contain millions of transistors
  Intel Pentium 4 (2000): 48 million
  IBM PowerPC 750FX (2002): 38 million
  IBM/Apple PowerPC G5 (2003): 58 million
Logically, each transistor acts as a switch
Combined to implement logic functions
  AND, OR, NOT
Combined to build higher-level structures
  Adder, multiplexer, decoder, register, …
Combined to build processor
  LC-3
Notes: Intel and Pentium are trademarks of Intel Corporation. IBM and PowerPC are trademarks of International Business Machines Corporation. Apple is a trademark of Apple Computer, Inc.

## Slide 26: Simple Switch Circuit
Switch open:
  No current through circuit
  Light is off
  Vout is +2.9V
Switch closed:
  Short circuit across switch
  Current flows
  Light is on
  Vout is 0V
Switch-based circuits can easily represent two states:
on/off, open/closed, voltage/no voltage.

## Slide 27: n-type MOS Transistor
MOS = Metal Oxide Semiconductor
  two types: n-type and p-type
n-type
  when Gate has positive voltage, short circuit between #1 and #2 (switch closed)
  when Gate has zero voltage, open circuit between #1 and #2 (switch open)
Gate = 1
Gate = 0
Terminal #2 must be
connected to GND (0V).

## Slide 28: p-type MOS Transistor
p-type is complementary to n-type
  when Gate has positive voltage, open circuit between #1 and #2 (switch open)
  when Gate has zero voltage, short circuit between #1 and #2 (switch closed)
Gate = 1
Gate = 0
Terminal #1 must be
connected to +2.9V.

## Slide 29: Logic Gates
Use switch behavior of MOS transistors to implement logical functions: AND, OR, NOT.
Digital symbols:
  recall that we assign a range of analog voltages to each digital (logic) symbol
  assignment of voltage ranges depends on electrical properties of transistors being used
    typical values for "1": +5V, +3.3V, +2.9V
    from now on we'll use +2.9V

## Slide 30: CMOS Circuit
Complementary MOS
Uses both n-type and p-type MOS transistors
  p-type
    Attached to + voltage
    Pulls output voltage UP when input is zero
  n-type
    Attached to GND
    Pulls output voltage DOWN when input is one
For all inputs, make sure that output is either connected to GND or to +, but not both!

## Slide 31: Inverter (NOT Gate)
In | Out
0 V | 2.9 V
2.9 V | 0 V
In | Out
0 | 1
1 | 0
Truth table

## Slide 32: NOR Gate
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Note: Serial structure on top, parallel on bottom.

## Slide 33: OR Gate
Add inverter to NOR.
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 34: NAND Gate (AND-NOT)
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Note: Parallel structure on top, serial on bottom.

## Slide 35: AND Gate
Add inverter to NAND.
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 36: Basic Logic Gates

## Slide 37: Combinatorial Gates
always @(a or b) y = a & b;
OR
assign y = a & b;

## Slide 38: Memory Elements
Latches
always @( LE or D )
if (LE == 1) Q = D;
Flip Flops
always ( posedge CLK ) Q = D;
Latches are level sensitive while flip flops are edge triggered.
12/16

## Slide 39: Memory Elements
Latches
always @( LE or D )
if (LE == 1) Q = D;
Flip Flops
always ( posedge CLK ) Q = D;
Latches are level sensitive while flip flops are edge triggered.
12/16

## Slide 40: Memory Elements
Latches
always @( LE or D )
if (LE == 1) Q = D;
Flip Flops
always ( posedge CLK ) Q = D;
Latches are level sensitive while flip flops are edge triggered.
12/16

## Slide 41: Memory Elements
Latches
always @( LE or D )
if (LE == 1) Q = D;
Flip Flops
always ( posedge CLK ) Q = D;
Latches are level sensitive while flip flops are edge triggered.
12/16

## Slide 42: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model
Sequential order of execution
Memory: Program and data storage Disk: File storage (passive data storage)
13/16

## Slide 43: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model Sequential order of execution
Memory: Program and data storage Disk: File storage (passive data storage)
13/16

## Slide 44: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model
Sequential order of execution
Memory: Program and data storage
Disk: File storage (passive data storage)
13/16

## Slide 45: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model Sequential order of execution
Memory: Program and data storage Disk: File storage (passive data storage)
13/16

## Slide 46: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model Sequential order of execution
Memory: Program and data storage
Disk: File storage (passive data storage)
13/16

## Slide 47: A Computer
Computer is a “machine”
As long as power is supplied, processor keeps executing instructions
Stored program model Sequential order of execution
Memory: Program and data storage Disk: File storage (passive data storage)
13/16

## Slide 48: Computer is a machine
I/O
MEMORY
CPU
14/16

## Slide 49: The machine is electronic
I/O
MEMORY
CPU
14/16

## Slide 50: Fetch-Execute-Store Model
Processor reads an instruction from memory
Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 51: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 52: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 53: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 54: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 55: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 56: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 57: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 58: Fetch-Execute-Store Model
Processor reads an instruction from memory Instruction:
A sequence of bits, understood and operated upon by processor
Processor interprets these bits and operates on data
Stored in internal registers or in memory
Result of the execution is stored in memory/registers. Processor continues fetching the next instruction. Program:
Collection of instructions that are fetched and executed one after another
15/16

## Slide 59: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Programs for Virtual machine:
16/16

## Slide 60: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Programs for Virtual machine:
16/16

## Slide 61: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16

## Slide 62: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16

## Slide 63: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16

## Slide 64: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16

## Slide 65: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16

## Slide 66: Fetch-Execute-Store Model
Processor takes program only as a sequence of bits
Machine Language
We understand programs in various forms
Assembly language: One to one correspondence with the machine language
High level languages:
Translators are needed to convert to machine language (compilers)
Programs for Virtual machine:
Languages such as Java, compile code to a virtual machine which is then interpreted by a tool.
16/16