## Slide 1: Number Representation
A number in a number system is represented using digits for that system

## Slide 2: Binary Number System
Binary system is as natural to a digital machine as decimal system to a man.
  Man has 10 fingers. Learns counting using that.
  Digital systems have to logic states
    0/1 or True/False, ON/OFF
A number in a number system is represented using digits to that system
Decimal digits are 0 to 9. Binary digits are 0 and 1.
Maximum value: bn−1. b: base, n: Number of digits.

## Slide 3: Number system
100011 can be a number at any base ≥ 2.
The value of a number is same irrespective of the base. For writing it on a paper we need a representation.
’b100011 is ’h23 or ’o43 or ’d35 …
’o100011 is ’h8009 or ’d32777.

## Slide 4: Hexadecimal Numbers
Base : 16
Symbols : 0-9, A-F (10-15)
Example1: (3AB8)16
=3*163+10*16^2+11*16+8
=15032
Example 2: (1111)H
=4096+256+16+1= 4369

## Slide 5: Converting Decimal to Hexa
Iteratively divide decimal number with 16. Remainder becomes right most digit.
Repeat the process with Quotient until quotient is less than 16.
Convert 234 to Hexadecimal.
Divide by 16: Quotient 14 (E), remainder: 10(A)
(234)16= EA

## Slide 6: Octal Representation
Base =8, Digits 0-7
(125)8=5+2*8+1*64=85
Converting Decimal to Octal
Just like Hexa, repeatedly devide quotient by 8, remainders make the octal digits (from least significant to most significant)
Example: Convert 235 to Octal
Divide by 8, Quotient 29, Remainder 3
Divide 29 by 8, Quotient 3, Remainder 5
(235)10= (353)8

## Slide 7: Binary Representation
Symbols (called bits or binary digits)=0,1
(10)10= (1010)2
How?
Divide by 2, Remainder 0, Quotient =5
Divide 5 by 2, Quotient 2, Remainder 1
Divide 2 by 2, Quotient 1, Remainder 0

## Slide 8: Converting Hexa to Binary
Each Hexa Digit can be written as 4 Bits
(2A3)16= (0010 1010 0011)2
Binary to Hexa:
Combine 4 bits to give one Hex Digit (starting from right most bit)
(101111001100)2 = (B C C)H
111011=(3B)16

## Slide 9: Converting Octal to Binary and Converse
Exactly like Hexa; Use 3 bits for an Octal Digit.
1011011= (133)8
(257)8 = 010 101 111

## Slide 10: Conversion from Hexa to Octal and Vice versa
First convert Hexa (Octal) to Binary and then convert Binary to Octal (Hexa)
1AB = 000110101011 = (0653)8
(756)8= 111101110 =1EE

## Slide 11: Addition and Subtraction
Use Carry and Borrow as normal addition/Substraction remembering the Base value. In Hexa a carry will be generated if the sum of digits exceeds 15. A borrow (worth 16) will be needed if the digit being substracted is larger.
1AB +23C =3E7
23C-1AB = 091=000010010001=

## Slide 12: Representation on a computer
Computers have a finite and fixed amount of storage for data types.
  n bit data type to contain integer can store only n bits of information.
Let’s first consider unsigned numbers (or only non-negative numbers)
  In n bits, maximum value is 2n−1.
  Minimum value is 0.
Typical values of n are 8, 16, 32, 64 etc.

## Slide 13: Signed numbers
Sign can be ‘+’ or ‘−’.
For a decimal number system, we use separate symbols to indicate the sign.
In binary number system, one bit is needed for sign.
  Say 0: for positive numbers and 1: for negative numbers.
Thus 5 is 0101 in binary and -5 is 1101 in binary.
But the story is a bit more complex here.

## Slide 14: Signed numbers
Sign magnitude representation.
  Sign as a bit (0: positive, 1: negative)
  Magnitude as unsigned number (in n−1 bits if total number of bits available are n)
  Maximum value: 2n−1−1. Minimum: −(2n−1−1).
  Two separate representations for +0 and −0.
2’s Complement number system
  Easy for computations. There is no separate signed addition/subtraction needed.

## Slide 15: 2’s complement number system
If n bits are available, we represent the positive numbers as unsigned numbers.
Negative numbers are first added 2n and then the resulting positive number is represented.
  Recall 2n is same as 0 if only n bits are used to represent the number.
Say n = 8. 2n = 256. Representation of 25 is 00011001. Representation of -25 is that of 231 (256 – 25) or 11100111.
Max Value: 2n−1−1. Min value: −2n−1
  Prove this as an exercise.

## Slide 16: 2’s complement numbers
To compute representation of a negative number faster,
  find the representation of its absolute value in n bits.
  invert all bits of this number and add 1 to it.
For example, consider -10 in 8 bits
  10 in 8 bits is 00001010.
  Invert all bits to get 11110101. Add 1 to it to get 11110110.

## Slide 17: 2’s complement makes arithmetic easy
Add bit patterns of two numbers irrespective of whether the numbers are positive or negative.
For subtraction A-B, use addition of A + (-B). –B can be found by 2’s complement.

## Slide 18: Adder and Subtractor

## Slide 19: Representation of Characters
Characters are coded.
  All I/O devices can only print characters.
  To print an integer first its corresponding character array representation need to be found and printed.
    printf function does that for us when %d is used.
ASCII coding
  American Standard Coding for Information Interchange
  See ‘man ascii’ for details.

## Slide 20: Representation of characters
Internationalization of scripts demanded more space for the characters.
Unicode character set
U+0000 to U+007F for English (ASCII equivalent)
Indian scripts are U+0900 to U+0D7F for Devanagari, Bengali, Gurumukhi, Gujrati, Oriya, Tamil, Telugu, Kannada, Malayalam.
  क (U+0915), ক (U+0995), ਕ (U+0A15), ક (U+0A95), க (U+0B95), క (U+0C15), ಕ (U+0C95), ക (U+0D15)

## Slide 21: Representation of Characters
With Unicode, the character coding and display are independent. Esp. so for Indian Scripts.
  U+0915 (क) U+094D(्), U+0915 (क) make up ‘क्क’.
Unicode Characters are supported in various programming languages. Java, wchar in C etc.