## Slide 1: What have we learnt so far?
The basic organization of a computing system.
The basic arithmetic and logic operations
performed by the computers.
We will now learn about the working of various units of a computing system.
We will start with the most important component of a computer, CPU.
We will also learn the addressing modes for
instructions.

## Slide 2: High Level Programming
C is a high level programming language.
High level languages resemble with natural languages (say English).
Programming is easy in high level languages.
Program in a high level language is called Source Program in that language.

## Slide 3: Machine Language Programming
However, the computer can understand only the language of 0s and 1s.
A program for the computer is therefore, a sequence of machine instructions.
A machine instruction is a sequence of 0s and 1s to the computer which a computer can understand, interpret and can carry out the required functions.
This sequence of machine instructions is called Machine Language Program or Object Code .

## Slide 4: Assembly Language Programming
Computer understands language of 0s and 1s (machine language).
Programming in machine language is difficult and error prone.
Assembly language is designed to simplify programming in machine language.
Each instruction is represented by a symbol in assembly language.
Makes program writing more convenient.
One to one correspondence between machine language and assembly language instruction.
Assembler generates machine code from assembly language program.

## Slide 5: Assembly Language Programming (contd.)
Not practical to write big programs in assembly language.
Software is written in high level languages like Pascal, C etc.
Each instruction in high level languages corresponds to several instructions in assembly language or machine language.
High-level language programming is generally machine-independent.

## Slide 6: A C statement
Consider the C statement
A = B + C
The corresponding assembly language code is
Load R2,[B]; Load the contents of
variable B in a high speed register.
Load R1,[C]; Load the contents of variable C in another high-speed register.
Add R1,R2 ; Add the contents of two registers.
Store R1,[A]; Store the result in the memory location assigned to A.

## Slide 7: Program to compute 2n
code fragment in C
count=n;
result = 1;
while (count >0)
{
result = result*2;
count = count -1;
}

## Slide 8: Assembly language program
Corresponding program in a hypothetical assembly language.
LOAD R1,[N] ; N is address containing n
MOVI R2,1 ; R2 stores the result
LOOP: CMP R1,0 ; Check if n=0
BLE EXIT ; Computation
; over if n<=0
MPYI R2,2 ; Multiply
; result by 2.
DCR R1 ; Decrement
; the count.
JMP LOOP ; Repeat the
; loop.
EXIT: STORE R2,[RESULT];Store result.

## Slide 9: Who performs these operations?
In order to perform the above sequence of operations, we need some circuitry.
We also need some circuitry which is capable of adding two numbers.
We also need some circuitry which can control the sequence of operations in order to execute the statement.
The part of the computer which performs these jobs is Central Processing Unit.

## Slide 10: Functions of Central Processing Unit
Fetches an instruction from memory.
Decodes and fetches operands for the instruction.
Executes the instruction.
Controls the timing of operations during execution.

## Slide 11: Components of CPU
Control Unit.
  Controls data transfer among various units within the CPU.
Arithmetic and Logic Unit.
  Performs various operations on operands under the control of control unit. Operands are fetched by the control unit.

## Slide 12: CPU Registers
High speed storage devices used to store data temporarily.
General Purpose Registers : Can be used for arithmetic and logic operations by the instructions.

## Slide 13: Special Purpose Registers
Instruction Register : Holds current instruction being executed.
Program Counter : Holds address of next instruction to be executed.
Stack Pointer :
  Part of main memory used as stack
  Stack accesses are done in a last-in-first-out manner.
  Stack pointer points to the top of stack.

## Slide 14: Instruction
An instruction consists of two parts:
  operation
  operand(s).
Some instructions can be without any operand.
Actual number of instructions, their formats and actual operation differ from processor to processor.

## Slide 15: Length of an instruction
In many processors, the instructions are of fixed lengths, i.e., each instruction occupies the same amount of memory space (mostly 16 bits or 32 bits).
However, in other processors like Intel 8085, 80386, 80486 etc. the length of instruction depends on type of operation, and number and type of its operands.
Zero Address Instructions : Don’t need any explicit operands.
Single Address Instruction : These instructions need one operand which can be either a register or a memory location.
Two/Three Address Instructions: Need two or three operands.
  Operands can be any combination of registers or memory locations.

## Slide 16: About this lecture
After learning about the basic CPU organization, its registers and parts of an instruction, in this lecture we will discuss the following:
Various types of machine instructions.
Various modes of specifying the address of an operand.
Machine instruction execution steps.

## Slide 17: Instruction Types
Instruction can be classified in four categories.
Data movement instructions
  between memory and registers.
  between registers.
Arithmetic and logic instructions.
Program sequencing and control instructions.
Input-Output instructions.

## Slide 18: Data Movement Instructions
From one register to another.
From one memory location to another.
From a register to memory location and from memory location to register.
Typical instructions for data transfer are Move, Load and Store.
Source and destination of data are either explicitly given with instruction or assumed implicitly.

## Slide 19: Arithmetic and Logic Instructions
Performs arithmetic operations such as:
  Addition, subtraction, multiplication, division, comparison etc..
Logical operations such as:
  Bitwise AND, OR, Ex-OR, complement etc.
Shift or rotate instructions such as
  Shift right, shift left etc.
Operands specified in the instruction

## Slide 20: Program Flow and Control Instructions
Normally, a program is executed in a sequence
Program counter holds the address of next instruction.
In sequential execution, program counter will be incremented by length of current instruction after the fetch is over.
This gives address of next instruction.
However, sometimes it is necessary to execute an instruction which is not at next memory location.
This is done by a branch instruction.
  unconditional branch (branch always).
  conditional branch (branch only if some condition is satisfied).

## Slide 21: Control Instructions (contd.)
Jump (unconditional branch to a specified instruction)
Conditional Jump (branch only if a condition is satisfied).
Call (execute a set of instructions called subroutine before coming back to next instruction in present sequence).
Conditional Call (similar to call but only if a condition is satisfied).
Return (returning from a subroutine).
Conditional Return (similar to return but only if condition is satisfied).

## Slide 22: Input Output Instructions
Communication between program and outside world through input-output devices.
Most of input output instructions need:
  Identification of input-output port.
  Data to be transferred
  Source/destination of data in the main memory.
Some I/O instructions are also used to set or reset interrupt masks.
Many I/O instructions are like memory to register data transfer instructions.

## Slide 23: Condition Codes
Specific bits of status register or condition code register.
Arithmetic and logic operations modify these values.
Some of commonly used flags are:
  zero flag (denotes if the result of last arithmetic operation is zero or denotes equality in case of comparison )
  sign flag (denotes positive or negative sign of result from last instruction)
  parity flag (even or odd number of 1s in the result)
  carry flag (carry in case of addition or borrow in case of subtraction)

## Slide 24: Addressing Modes
Refers the way in which operand of an instruction is specified.
All addressing modes need not be supported by all processor architectures.

## Slide 25: Addressing Modes
Register Addressing Mode:
Operand(s) is(are) contents of CPU register(s) whose name is (are) one of the following:
  Explicitly given in instruction
  Known implicitly (for example, modifying a special purpose register).
Immediate Addressing Mode:
  Operand is given in the instruction itself.

## Slide 26: Addressing Modes (contd.)
Direct Addressing Mode:
  Operand is in a memory location whose address is explicitly specified in the instruction.
• Indirect Addressing Mode:
  Address of operand is in a register or main memory location.
  Register indirect addressing mode if the address is specified in a register.
  Memory indirect addressing mode if the address is specified in a memory location.

## Slide 27: Addressing Modes (contd.)
Indexed Addressing Mode:
In general,
  Effective address of operand = displacement + contents of a base register + contents of index register * scaling factor where displacement or offset is a constant specified in the instruction.

## Slide 28: Indexed Addressing Mode (contd.)
Different types of indexed addressing possible using only some of the parameters in the above formula used.
  scaled direct register indexed addressing (all parameters used).
  direct register indexed addressing (all parameters used except scaling factor).
  direct indexed addressing (all parameters used except scaling factor and contents of base register).
  register (or base) indexed addressing (all parameters used except scaling factor and displacement).

## Slide 29: Addressing Modes (contd.)
Autoincrement/autodecrement Mode:
Address of operand is stored in specified register. The contents of the register are incremented/ decremented before or after accessing the data.
  Post-increment
  Pre-increment
  Post-decrement
  Pre-decrement

## Slide 30: Instruction Execution Steps
Fetch - Bring instruction from memory to instruction register.
Decode - Find operation to be performed and address of operands.
Operand fetch - get operands and keep them ready for ALU.
Execute- Perform required operation by sending control signals to various units of CPU.
Result store - write the results of execution in a register or memory.
Time taken to execute an instruction depends upon
  complexity of instruction
  number of operands
  addressing mode etc.